## Slide 1
ECEN 4/5632 Theory and Application of Digital Filters
Lecture 2, 8-25-26, 8-27-26
Peter Mathys*
* With generous help from Gemini Pro and ChatGPT

## Slide 2
DSP + ML
Eigenfunctions and
the DTFT
Week 1 • Lecture 2 • 75 minutes
Why sinusoids survive LTI systems—and why frequency-domain multiplication is so powerful
e^{jωn}
probe
LTI system
h[n]
H(e^{jω})
eigenvalue
DTFT
spectrum
Features
spectrogram
Notes: Timing: 2 min. Ask: if a pure tone enters an LTI filter, what can change—frequency, amplitude, phase?

## Slide 3
Today’s learning objectives
Move from time-domain mechanics to frequency-domain structure.
00–10 MIN
Prove that complex exponentials are eigenfunctions of LTI systems.
Define the DTFT and inverse DTFT and explain 2π periodicity.
Use time shift, convolution, and Parseval properties.
Derive frequency response directly from a linear constant-coefficient difference equation.
Interpret a one-pole filter in time and frequency domains.
Graduate expectation
Be able to state convergence or stability assumptions when a transform/frequency response is used.
Notes: Timing: 3 min.

## Slide 4
Recap: an LTI system is convolution by h[n]
Now choose an input that makes convolution simplify dramatically.
00–10 MIN
Notice
The input waveform e^{jωn} factors back out. The system can only multiply it by a complex number.
Notes: Timing: 4 min. This is the proof. Keep emphasizing what depends on n and what does not.

## Slide 5
Complex exponentials are eigenfunctions of every LTI system
The eigenvalue depends on frequency.
00–10 MIN
What stays the same
What changes
Frequency ω
Exponential form
Infinite-duration mode
Magnitude: |H(e^{jω})|
Phase: ∠H(e^{jω})
Possibly complete cancellation
Notes: Timing: 4 min. Use ordinary sinusoids as real parts of exponentials. An LTI system cannot generate a new frequency from a single sinusoid.

## Slide 6
Frequency response is a gain-and-phase lookup table
One complex number for each normalized frequency ω.
10–35 MIN
Tone in
cos(ω₀n)
Magnitude
× |H(e^{jω₀})|
Phase
+ ∠H(e^{jω₀})
Tone out
same ω₀
Audio EQ
A graphic equalizer is approximately a deliberately shaped |H(e^{jω})|.
Notes: Timing: 4 min. Bridge from eigenfunction proof to intuitive filter behavior.

## Slide 7
The DTFT analyzes a sequence as a continuous function of frequency
Time is discrete; frequency remains continuous.
10–35 MIN
Forward DTFT
Inverse DTFT
Sequence x[n] → function X(e^{jω})
Weighted sum of rotating phasors
Requires convergence in an appropriate sense
Integrates one period of spectrum
Reconstructs each integer sample
Any interval of length 2π works
Notes: Timing: 6 min. Mention absolute summability as a simple sufficient condition for ordinary convergence; do not derail into distributions unless desired.

## Slide 8
Why is the DTFT 2π-periodic?
Because sampled-time exponentials cannot distinguish ω from ω+2πk.
10–35 MIN
−2π
−π
0
π
2π
same spectral content repeats every 2π
Notes: Timing: 5 min. Instructor tip: point ahead to sampling/aliasing. π rad/sample corresponds to the Nyquist frequency after a sampling rate is specified.

## Slide 9
Normalized frequency ↔ physical frequency
Week 2 will make this relationship central.
10–35 MIN
Example
At f_s=48 kHz: ω=π/2 ↔ 12 kHz, and ω=π ↔ 24 kHz.
The interval −π≤ω<π represents one unique frequency period.
Frequencies outside that interval wrap into it modulo 2π.
Notes: Timing: 4 min. This slide sets up the Week 2 sampling lecture without teaching aliasing yet.

## Slide 10
Two DTFT pairs worth knowing immediately
Use them as anchors—not as a substitute for reasoning.
10–35 MIN
Why the condition?
For |a|<1, the geometric series is absolutely summable; |a|≥1 does not converge on the unit circle in the ordinary sense.
Notes: Timing: 4 min. The a^n u[n] pair will be reused for the one-pole system.

## Slide 12
Time shifting becomes linear phase
Delays are easy to recognize in the frequency domain.
35–55 MIN
Magnitude
Phase
|e^{-jωn₀}|=1
A pure delay does not change spectral magnitude
Adds −ωn₀ radians
Linear phase slope encodes delay
Audio connection
An ideal sample delay preserves the spectrum’s magnitude exactly; it only rotates phase versus frequency.
Notes: Timing: 4 min.

## Slide 13
Convolution in time ↔ multiplication in frequency
This is one of the most important DSP simplifications.
35–55 MIN
Time domain
slide / multiply / sum
DTFT
transform
Frequency domain
pointwise multiply
IDTFT
reconstruct
Computational echo
FFT-based convolution exploits the same multiplication idea numerically for long signals.
Notes: Timing: 6 min. Sketch the proof by substituting y[n]=Σx[k]h[n−k] into the DTFT and changing variables. Avoid drowning in indices; focus on the separation into X times H.

## Slide 14
Parseval: energy is preserved across representations
The spectrum redistributes energy; it does not create it.
35–55 MIN
Time-domain view
Frequency-domain view
Energy = sum of squared samples
Natural for waveforms
Energy density across ω
Natural for bands and features
ML bridge
Many audio features—band energies, log spectra, mel features—summarize how signal energy is distributed across frequency.
Notes: Timing: 4 min. Clarify that mel scaling and log magnitude are later nonlinear transformations; Parseval applies before those.

## Slide 15
Difference equations give H(e^{jω}) directly
Use the eigenfunction or DTFT property instead of solving every input separately.
35–55 MIN
Substitute x[n]=e^{jωn}, y[n]=H(e^{jω})e^{jωn}.
Factor out e^{jωn}.
Solve the remaining algebraic equation for H(e^{jω}).
Notes: Timing: 5 min. Students should understand this as the same eigenfunction argument, not a separate trick.

## Slide 16
One-pole example: y[n]=0.5y[n−1]+x[n]
A simple recursive smoother with a strong low-frequency preference.
55–75 MIN
At ω=0
At ω=π
H=1/(1−0.5)=2
DC is amplified
H=1/(1+0.5)=2/3
Nyquist-frequency alternation is attenuated
Notes: Timing: 5 min. Ask students to predict low-pass vs high-pass before plotting.

## Slide 17
Think–Pair–Share: sketch |H(e^{jω})| before computing
Reason from a few strategically chosen frequencies.
55–75 MIN
Given y[n] = 0.5y[n−1] + x[n]
1 minute: derive H(e^{jω}).
2 minutes: evaluate |H| at ω=0, π/2, π.
2 minutes: sketch a smooth 2π-periodic magnitude curve.
Pair discussion: what audio behavior would you expect?
Prompt
What feature of the recursion causes “memory” of prior samples?
Graduate extension
Relate the coefficient 0.5 to a pole at z=0.5 and explain why moving it toward 1 increases low-frequency selectivity.
Notes: Timing: 5 min active work. Do not reveal the next slide until pairs have committed to a sketch.

## Slide 18
Think–Pair–Share solution
The denominator is smallest near ω=0, so the response peaks at low frequency.
55–75 MIN
Chart: 
| −π | 0 | π
¦H¦ | 0.66667 | 0.66953 | 0.67824 | 0.69313 | 0.71481 | 0.74421 | 0.78262 | 0.83186 | 0.89443 | 0.97363 | 1.0738 | 1.2 | 1.3572 | 1.5457 | 1.7511 | 1.9273 | 2 | 1.9273 | 1.7511 | 1.5457 | 1.3572 | 1.2 | 1.0738 | 0.97363 | 0.89443 | 0.83186 | 0.78262 | 0.74421 | 0.71481 | 0.69313 | 0.67824 | 0.66953 | 0.66667
Three checkpoints
ω=0: 2 • ω=π/2: 0.894 • ω=π: 0.667
Interpretation
Smooth low-pass tendency • recursive memory • stable because |0.5|<1
Notes: Timing: 4 min. Point out periodic continuation beyond ±π.

## Slide 19
Python demo: freqz and filtering
The numerical tools should confirm—not replace—the analysis.
55–75 MIN
SciPy frequency response
import numpy as np
from scipy import signal
b = [1.0]
a = [1.0, -0.5]
w, H = signal.freqz(b, a, worN=1024)
mag = np.abs(H)
Filtering
x = np.random.randn(48000)
y = signal.lfilter(b, a, x)
# Compare spectra / listen if desired
Notebook task
Change the recursion coefficient from 0.5 → 0.9 → 0.99. Predict the shape first; then verify with freqz.
Notes: Timing: 4 min. Use the provided notebook cell.

## Slide 20
DTFT vs DFT vs FFT
Three related terms that students often collapse into one.
55–75 MIN
DTFT
DFT / FFT
Input: discrete-time sequence
Frequency: continuous ω
2π-periodic spectrum
Mathematical transform
Input: finite N samples
Frequency: N discrete bins
DFT is the transform
FFT is an algorithm for the DFT
Practical bridge
In code, we sample the DTFT-like spectrum on a finite grid using the DFT/FFT. The grid and window matter.
Notes: Timing: 4 min. This prevents a major vocabulary problem before later spectrogram work.

## Slide 21
ML bridge: spectrograms are structured frequency-domain features
The DTFT is the conceptual ancestor of the STFT.
BRIDGE
Waveform
x[n]
Window
local segment
DTFT/DFT
local spectrum
Stack over time
spectrogram
CNN
learn patterns
DSP explains what the axes and magnitudes mean.
Windowing and sampling choices determine resolution and leakage.
ML operates on features whose structure comes directly from signal-processing choices.
Notes: Timing: 3 min. Preview: later weeks will build spectrograms and feed them to models.

## Slide 22
Concept check
Reason from the denominator, not from memorized filter labels.
CHECK
For H(e^{jω}) = 1/(1 − 0.9e^{−jω}), where is |H| largest?
A. Near ω=0
B. Near ω=π/2
C. Near ω=π
D. It is constant for all ω
Notes: Timing: 2 min. Correct answer A.

## Slide 23
Concept check
Reason from the denominator, not from memorized filter labels.
CHECK
For H(e^{jω}) = 1/(1 − 0.9e^{−jω}), where is |H| largest?
A. Near ω=0
B. Near ω=π/2
C. Near ω=π
D. It is constant for all ω
Correct: at ω=0 the terms 1 and 0.9e^{-jω} nearly cancel in the denominator, making the magnitude large.
Notes: Timing: 2 min. Correct answer A.

## Slide 24
Lecture 2 synthesis
The frequency domain turns LTI systems into multiplication.
WRAP-UP
Complex exponential
e^{jωn}
Eigenvalue
H(e^{jω})
DTFT
X(e^{jω})
Convolution theorem
Y=XH
Spectral features
energy / shape
Be able to derive H(e^{jω}) from h[n] or a difference equation.
Be able to explain 2π periodicity and the relation ω=2πf/fs.
Be able to reason qualitatively about a response before plotting it.
Week 2
Sampling will explain which analog frequencies map to the same discrete-time frequency—and why aliasing occurs.
Notes: Timing: 3 min. Exit ticket: “Why can an LTI system change the amplitude and phase of a sinusoid but not its frequency?”