## Slide 1
ECEN 4/5632 Theory and Application of Digital Filters
Lecture 8, 9-17-26
Peter Mathys*
* With generous help from Gemini Pro and ChatGPT

## Slide 2
Midterm Exam 1
Thursday September 24, 9:30 – 10:45 am, ECCR 131 for in-class students.
Between Sep. 24 and Sep. 30 for on-line students who must supply email address of exam proctor.
Covers Lectures 1 through 8 and Problem Sets 1 through 4
Exam problems will be similar to Problem Set questions
Closed book, notes, no cheat sheets. Reference formulas will be printed on exam.
No laptops, tablets, phones, basic scientific calculator o.k.

## Slide 3
WEEK 4 ● LECTURE 8
IIR Design, Bilinear Transformation, & Data Preprocessing
From analog prototypes to stable digital filters—and the phase choices hidden in ML preprocessing
analog prototypes
→
bilinear map
→
prewarping
→
offline ML
75 minutes • senior + first-year graduate ECE
Oppenheim & Schafer + Raschka

## Slide 4
ROADMAP
Where this 75-minute lecture is going
2
0–15 min • Analog prototypes
Butterworth, Chebyshev I/II, and elliptic tradeoffs.
15–40 min • Bilinear transform
Map the analog LHP into the digital unit disk while preserving stability.
40–60 min • Warping + prewarp
Derive Ω(ω) and hit the desired digital critical frequencies.
60–75 min • ML preprocessing
Causal IIR versus forward-backward zero-phase filtering and deployment implications.
DSP bridge: IIR design gives efficient recursive filters; ML preprocessing must also account for phase, causality, and train/deployment consistency.
Classical DSP supplies structure and constraints; machine learning either reuses that structure or learns parameters inside it.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 5
IIR MOTIVATION
Why accept feedback and nonlinear phase?
3
Efficiency
Sharp magnitude selectivity can often be obtained with far fewer coefficients than an FIR meeting comparable magnitude specifications.
Tradeoff
The recursive denominator introduces poles and typically nonlinear phase / frequency-dependent group delay.
ML preprocessing
For offline denoising or smoothing, compact IIR filters are attractive—but preprocessing must match the temporal assumptions of deployment.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 6
ANALOG PROTOTYPES
Four classical ways to spend ripple and transition width
4
Butterworth
Maximally flat magnitude in the passband; monotonic.
Chebyshev
Spend ripple in one band to sharpen the transition.
Elliptic
Ripple in both bands; steepest transition for a given order/specification.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 7
Magnitude and Phase of Analog Lowpass Prototypes

## Slide 8
BUTTERWORTH
Maximally flat magnitude response
5
Order N
Higher N steepens the transition around Ω_c.
No passband ripple
Butterworth is attractive when smooth magnitude behavior matters more than the narrowest possible transition.
Good answer
At the cutoff, the squared magnitude is 1/2 regardless of N.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 9
Magnitude, Phase, and Pole-Zero (in s-Plane) Plots for Analog Designs

## Slide 10
BUTTERWORTH
What increasing order buys—and what it costs
6
Magnitude slope
Each additional pole increases asymptotic attenuation by about 20 dB/decade.
Implementation cost
Higher order means more states / sections and greater numerical sensitivity in direct-form implementations.
Practice
Use second-order sections for moderate/high-order digital IIR implementations when possible.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 11
PROTOTYPE TRADEOFFS
Where the ripple is allowed to live
7
Prototype
Passband
Stopband
Transition / comment
Butterworth
monotonic
monotonic
maximally flat; smooth
Chebyshev I
equiripple
monotonic
sharper for allowed passband ripple
Chebyshev II
monotonic
equiripple
spend ripple in stopband
Elliptic
equiripple
equiripple
steepest transition for given order/spec
Engineering habit
Choose the prototype from passband/stopband tolerances and order requirements—not from a universal ranking.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 12
CONCEPT CHECK
Which prototype sounds plausible?
8
A • Sensor calibration
Passband amplitude must be smooth; moderate transition width is acceptable.
B • Tight transition
A small amount of controlled passband ripple is acceptable to lower order.
C • Most aggressive
Ripple is acceptable in both bands and minimum order is important.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 13
CONCEPT CHECK
Which prototype sounds plausible?
8
A • Sensor calibration
Passband amplitude must be smooth; moderate transition width is acceptable.
Good answer
Butterworth is a natural first choice because it is monotonic and maximally flat.
B • Tight transition
A small amount of controlled passband ripple is acceptable to lower order.
Good answer
Chebyshev I trades passband ripple for a sharper transition.
C • Most aggressive
Ripple is acceptable in both bands and minimum order is important.
Good answer
Elliptic is often the most aggressive classical choice.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 14
ANALOG → DIGITAL
What must a useful domain map preserve?
9
Stability
Analog stable poles satisfy Re{s}<0. They must map to |z|<1.
Frequency axis
The analog jΩ axis should map to the digital unit circle z=e^{jω}.
One-to-one mapping
Avoid aliasing of multiple analog frequencies onto the same digital frequency.
The bilinear transform satisfies these properties—but its price is nonlinear frequency warping.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 15
BILINEAR TRANSFORM
The substitution that maps the half-plane to the disk
10
Interpret T
T is the sampling period used in the analog-to-digital mapping.
Important
This is not the impulse-invariance map z=e^{sT}. The bilinear transform avoids frequency aliasing but warps the axis.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 18
STABILITY MAPPING
Why the analog left-half plane lands inside the unit circle
11
Good answer
The negative real part makes the numerator magnitude smaller than the denominator magnitude, so a stable analog pole maps inside the digital unit circle.
Boundary
For σ=0, numerator and denominator magnitudes are equal, hence |z|=1.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 19
STABILITY MAPPING
Representative analog stable poles map inside |z|=1
12
Interpretation
Every shown analog pole has negative real part. After the bilinear map, every digital pole lies strictly inside the unit circle.
This is the guarantee we want
Start from a stable analog prototype and the mapped digital filter remains stable, barring numerical implementation issues.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 20
FREQUENCY MAPPING
The analog jΩ axis maps exactly onto the unit circle
13
Endpoints
Ω=0 maps to ω=0. As |Ω|→∞, the digital frequency approaches ±π and z approaches −1.
No aliasing
The entire analog frequency axis maps one-to-one into −π<ω<π.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 21
FREQUENCY WARPING
The price of the one-to-one map
14
Low frequency
For small ω, tan(ω/2)≈ω/2, so Ω≈ω/T.
Near Nyquist
The map becomes strongly nonlinear; equal analog frequency intervals do not remain equal digital intervals.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 22
FREQUENCY WARPING
Near Nyquist, the analog axis is stretched dramatically
15
Read the curve
The relationship is nearly linear near DC but diverges as ω→π.
Design consequence
If you design the analog cutoff at the unwarped numeric value, the final digital cutoff misses its target.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 23
PREWARPING
Design the analog prototype at the frequency that maps to the desired digital edge
16
Design sequence
1 • Digital spec
ω_p, ω_s, ripple / attenuation
2 • Prewarp
map each critical digital frequency to Ω
3 • Analog design
design Butterworth / Chebyshev / elliptic prototype
4 • Bilinear map
substitute s(z) to obtain the digital filter
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 24
Bilinear Transform
s to z plane
Prewarp
Prewarping Digital Specification and Using Bilinear Transform to Convert Analog Prototype to Digital IIR

## Slide 25
WORKED EXAMPLE
Prewarp a desired cutoff at 0.4π rad/sample
17
Meaning
Design the analog prototype at Ω_c≈1.4531—not at 0.4π≈1.2566.
Check
After the bilinear transform, the measured −3 dB point lands at approximately 0.4π.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 26
Verify the Digital Design after Bilinear Transform

## Slide 27
DESIGN WORKFLOW
From digital specification to digital IIR
18
Digital requirements
ω_p, ω_s, A_p, A_s
→
Prewarp
Ω_p, Ω_s
→
Analog prototype
H_c(s)
→
Bilinear transform
H(z)
→
Verify
freqz + numerical stability
The bilinear transform preserves stability, not exact frequency spacing. Verification is part of the design, not an optional afterthought.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 28
IMPLEMENTATION
Explicit analog prototype → bilinear transform in SciPy
19
wc = 0.4*np.pi T = 1.0 Omega_c = (2/T)*np.tan(wc/2) b_a, a_a = signal.butter(4, Omega_c, analog=True) b_z, a_z = signal.bilinear(b_a, a_a, fs=1/T) w, H = signal.freqz(b_z, a_z)
Why show the explicit path?
It makes prewarping and the analog prototype visible instead of hiding the mathematics inside one convenience function.
Implementation practice
For deployment, prefer numerically robust second-order-section forms when order becomes substantial.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 29
VERIFICATION
The prewarped design hits the intended digital cutoff
20
Target
Desired digital cutoff: ω_c = 0.4π.
Measured
The script finds the −3 dB point at ≈0.3999π.
Good habit
Always verify the digital response after mapping.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 30
IIR PHASE
Efficient magnitude selectivity does not usually preserve waveform shape
21
Nonlinear phase
The phase is not a straight line in ω, so group delay varies with frequency.
ML implication
If timing relationships are part of the feature, causal IIR preprocessing can alter them. That may or may not matter depending on the task.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 31
IIR PHASE
Frequency-dependent group delay makes the distortion easier to see
22
Contrast with Lecture 7
The symmetric FIR had nearly constant τ_g. Here the delay changes across the passband/transition.
Practical question
Does the downstream model care about absolute timing, relative timing, or only long-term spectral statistics?
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 32
Group Delay for the Different IIR Filter Types

## Slide 33
What Happens if or ?
Poles congregate near . Finite numerical precision can lead to instability.

## Slide 34
OFFLINE PREPROCESSING
Forward-backward filtering cancels phase
23
Net phase
For real-coefficient filters, the phases cancel: zero-phase distortion.
But magnitude changes
The magnitude is squared, so attenuation in dB is approximately doubled.
And causality is gone
The backward pass uses future samples relative to a streaming implementation.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 36
OFFLINE PREPROCESSING
Compare causal IIR delay with forward-backward zero phase
24
Causal filter
The transient is delayed and reshaped according to the filter phase/group delay.
Forward-backward
The transient aligns much more closely in time—but the method is offline and noncausal.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 37
FORWARD-BACKWARD FILTERING
Zero phase does not mean “the same filter twice for free”
25
One pass
Magnitude is |H|.
Two passes
Magnitude becomes |H|²; order/effective selectivity are increased.
Design implication
If you need a final −3 dB edge after forward-backward filtering, design with the two-pass response in mind.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 38
CAVEATS
Zero-phase preprocessing can quietly change the learning problem
26
Noncausal
Future samples are used; not reproducible in a strict real-time stream.
Boundary transients
Finite-record initial conditions and padding can distort the beginning/end.
Magnitude squared
The effective response is not the same as one causal pass.
Train/serve skew
A model trained with future-aware filtering may see a different distribution when deployed causally.
Good engineering question: “Will the exact same preprocessing be available when the model is actually used?”
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 39
ML PIPELINE
Where a classical IIR can fit
27
Raw signal
sensor / audio
→
Fixed IIR
remove nuisance band
→
DSP features
MFCCs, energy, flux
→
Classifier
SVM / RF / MLP
Appropriate example
A known high-frequency interference band is irrelevant to the classification task and can be attenuated efficiently before features are computed.
Question before filtering
Could the “noise” contain class information? Fixed preprocessing is an inductive assumption and should be validated.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 40
DESIGN CHOICE
FIR, IIR, or learned front end?
28
Choice
Strength
Cost / risk
Good fit
Linear-phase FIR
controlled phase + finite support
more taps / delay
waveform alignment matters
IIR
sharp response with few coefficients
nonlinear phase; feedback
efficient causal preprocessing
filtfilt IIR
zero phase offline
noncausal; |H|²; edges
offline dataset preparation
Learned Conv1d
task-adaptive front end
needs data/validation
end-to-end models
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 41
WRAP-UP
Lecture 8 synthesis
29
Prototype
Choose where ripple is allowed and how much transition width you need.
Bilinear map
Stable analog LHP → stable digital unit disk.
Prewarp
Critical frequencies must be mapped through tan(ω/2).
Preprocessing
Phase, causality, edges, and deployment consistency are part of the ML problem.
Minute paper: Why can a zero-phase offline preprocessing pipeline give misleading confidence about a streaming deployment?
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka