## Slide 1
ECEN 4/5632 Theory and Application of Digital Filters
Lecture 9, 9-22-26
Peter Mathys*
* With generous help from Gemini Pro and ChatGPT

## Slide 2
Midterm Exam 1
Thursday September 24, 9:30 – 10:45 am, ECCR 131 for in-class students.
Between Sep. 24 and Sep. 30 for on-line students who must supply email address of exam proctor.
Covers Lectures 1 through 8 and Problem Sets 1 through 4
Exam problems will be similar to Problem Set questions
Closed book, notes, no cheat sheets. Reference formulas will be printed on exam.
No laptops, tablets, phones, basic scientific calculator o.k.

## Slide 3
WEEK 5 ● LECTURE 9
Time/Frequency Responses and Group Delay
From pole-zero geometry to waveform dispersion and all-pass phase equalization
pole-zero geometry → group delay → all-pass → ML feature timing
75 minutes • senior + first-year graduate ECE
Equations typeset in standard mathematical notation

## Slide 4
DSP + Machine Learning • Week 5
Roadmap
Oppenheim & Schafer + Raschka
2
0–15 min • Read magnitude and phase directly from pole-zero geometry.
15–40 min • Distinguish phase delay from group delay and connect nonlinear phase to dispersion.
40–60 min • Build all-pass systems from reciprocal pole-zero structure.
60–75 min • Ask whether preprocessing preserves the timing features an ML model actually uses.

## Slide 5
DSP + Machine Learning • Week 5
Frequency response is the z-transform evaluated on the unit circle
Oppenheim & Schafer + Raschka
3
Every digital frequency ω corresponds to one point e^(jω) on the unit circle.
Magnitude and phase can be read geometrically from vectors drawn from poles and zeros to that point.

## Slide 6
DSP + Machine Learning • Week 5
Pole-zero geometry: magnitude is a distance ratio
Oppenheim & Schafer + Raschka
4
Interpretation
Zeros pull the response toward zero when the unit-circle point passes nearby. Poles push the response upward when the unit-circle point passes nearby.

## Slide 7
DSP + Machine Learning • Week 5
Pole-zero geometry: phase is an angle sum
Oppenheim & Schafer + Raschka
5
Each zero contributes a vector angle.
Each pole contributes a vector angle with the opposite sign.
Phase can vary rapidly even when magnitude looks smooth.

## Slide 8
DSP + Machine Learning • Week 5
Worked geometry example
Oppenheim & Schafer + Raschka
6
At ω=0
The unit-circle point is z=1. The zero-distance is 0.2 and pole-distance is 0.5, so |H(1)|=0.4.
At ω=π
The point is z=-1. The distances are 1.8 and 1.5, so |H(-1)|=1.2. Predict a high-frequency tilt before plotting.

## Slide 9
Worked geometry example

## Slide 10
Worked geometry example

## Slide 11
Worked geometry example

## Slide 12
DSP + Machine Learning • Week 5
Concept check: move a pole toward the unit circle
Oppenheim & Schafer + Raschka
7
A pole at angle ω₀ moves radially from radius 0.5 to radius 0.95. What happens near ω₀?

## Slide 13
DSP + Machine Learning • Week 5
Concept check: move a pole toward the unit circle
Oppenheim & Schafer + Raschka
7
A pole at angle ω₀ moves radially from radius 0.5 to radius 0.95. What happens near ω₀?
Good answer: the denominator vector becomes much shorter, so magnitude increases sharply and the phase changes more rapidly.
Graduate-level addition: the pole also produces a more concentrated group-delay contribution near its angle.

## Slide 14
DSP + Machine Learning • Week 5
Phase delay and group delay answer different questions
Oppenheim & Schafer + Raschka
8
Phase delay
For a single sinusoidal component, how much phase corresponds to an equivalent delay?
Group delay
For a narrowband packet, how does the envelope / modulation arrive versus frequency?
Do not conflate them
They are equal for pure linear phase through the origin, but generally differ.

## Slide 15
DSP + Machine Learning • Week 5
Linear phase gives constant group delay
Oppenheim & Schafer + Raschka
9
All passband frequency components receive the same local delay.
The constant β can shift phase without changing the group-delay slope.
Possible π jumps from a real amplitude sign change should not be mistaken for physical dispersion.

## Slide 16
DSP + Machine Learning • Week 5
Nonlinear phase produces frequency-dependent delay
Oppenheim & Schafer + Raschka
10
Read both plots
The phase curvature becomes group-delay variation. The derivative makes rapid phase changes easier to interpret as timing dispersion.

## Slide 17
DSP + Machine Learning • Week 5
A transient is a superposition of many frequencies
Oppenheim & Schafer + Raschka
11
A sharp onset or pulse requires many spectral components.
If each component experiences a different delay, the components no longer reassemble at the same relative times.
The result can be peak shift, ringing, smearing, or altered onset slope—even if |H(e^(jω))| looks acceptable.

## Slide 18
DSP + Machine Learning • Week 5
Demonstration: causal IIR dispersion versus zero-phase offline filtering
Oppenheim & Schafer + Raschka
12
Good observation
The causal IIR can shift and reshape the transient. Forward-backward filtering restores timing much better, but it is noncausal and changes the effective magnitude response.

## Slide 19
Causal IIR dispersion versus zero-phase offline filtering

## Slide 20
Causal IIR dispersion versus zero-phase offline filtering

## Slide 21
DSP + Machine Learning • Week 5
All-pass systems: magnitude one does not mean “does nothing”
Oppenheim & Schafer + Raschka
13
An all-pass changes phase without changing magnitude.
That makes it a phase / group-delay design element rather than a magnitude-shaping element.
Useful for phase equalization, fractional-delay structures, and decomposing a system into minimum-phase and all-pass parts.

## Slide 22
DSP + Machine Learning • Week 5
First-order all-pass structure
Oppenheim & Schafer + Raschka
14
Pole at z=a lies inside the unit circle.
Zero at z=1/a* lies at the conjugate reciprocal location outside the unit circle.
On |z|=1, numerator and denominator distances match, so magnitude is unity.

## Slide 23
DSP + Machine Learning • Week 5
Phase equalization with an all-pass
Oppenheim & Schafer + Raschka
16
Suppose a magnitude response is acceptable but group delay is uneven.
Cascading an all-pass leaves total magnitude unchanged because |Hₜₒₜ|=|H||Hₐₚ|=|H|.
Choose the all-pass phase so its group-delay contribution makes the total delay flatter over the band of interest.

## Slide 24
DSP + Machine Learning • Week 5
What can an all-pass equalizer not fix?
Oppenheim & Schafer + Raschka
17
It cannot repair magnitude notches, stopband leakage, or insufficient bandwidth because its magnitude is exactly one.
It can only redistribute phase / group delay.
A causal stable all-pass generally adds nonnegative group delay; “flattening” often means adding delay where the original system was too fast rather than subtracting delay where it was too slow.

## Slide 25
DSP + Machine Learning • Week 5
ML context: feature distortion happens before the model
Oppenheim & Schafer + Raschka
18
ECG anomaly detection: QRS peak timing and slope may be predictive.
Audio event detection: onset rise time and inter-channel timing may be predictive.
Vibration fault detection: impulse spacing and envelope timing may be predictive.
A preprocessing filter that disperses these structures changes the features before an SVM, RF, MLP, or CNN can use them.

## Slide 26
DSP + Machine Learning • Week 5
Good ML engineering question
Oppenheim & Schafer + Raschka
19
Ask before filtering
Does the downstream task depend primarily on long-term spectral magnitude, or on timing / waveform morphology?
If magnitude statistics dominate, nonlinear phase may be harmless.
If local timing is predictive, preserve phase or make training/deployment use the same causal distortion.
Do not assume “denoised” means “more informative for the classifier.”

## Slide 27
DSP + Machine Learning • Week 5
Python demo: inspect response and delay
Oppenheim & Schafer + Raschka
20
b = np.array([1.0, -0.8])
a = np.array([1.0, -0.5])
w, H = signal.freqz(b, a, worN=2048)
phase = np.unwrap(np.angle(H))
w_gd, gd = signal.group_delay((b, a), w=2048)
# Pole-zero geometry
zeros = np.roots(b)
poles = np.roots(a)
# Compare causal IIR and zero-phase offline filtering
y_causal = signal.sosfilt(sos, x)
y_zero = signal.sosfiltfilt(sos, x)

## Slide 28
DSP + Machine Learning • Week 5
Concept check
Oppenheim & Schafer + Raschka
21
Two filters have identical |H(e^(jω))| but different ∠ H(e^(jω)). Must their outputs be identical for every input?

## Slide 29
DSP + Machine Learning • Week 5
Lecture 9 synthesis
Oppenheim & Schafer + Raschka
22
Pole-zero distance ratios explain magnitude; vector-angle sums explain phase.
Group delay turns phase slope into a timing diagnostic.
All-pass systems have unit magnitude but can strongly reshape phase and delay.
ML preprocessing must preserve—or consistently reproduce—the temporal features the model needs.