## Slide 1
ECEN 4/5632 Theory and Application of Digital Filters
Lecture 11, 10-01-26, 10-06-26, 10-13-26
Peter Mathys*
* With generous help from Gemini Pro and ChatGPT

## Slide 2
WEEK 6 ● LECTURE 11
The DFT and Fast Convolution
From frequency samples to efficient streaming FIR filtering
Oppenheim & Schafer • DFT / FFT / STFT | Raschka • CNN architecture and feature pipelines

## Slide 3
Learning objectives
ROADMAP
0:00–0:03
WEEK 10 • TIME-FREQUENCY ANALYSIS
• Interpret the N-point DFT as samples of the DTFT of a finite record.
• Distinguish linear convolution from N-point circular convolution.
• Choose zero-padding so DFT multiplication produces linear convolution.
• Explain and implement overlap-add and overlap-save block filtering.
• Connect FFT block processing to real-time preprocessing before ML inference.
Core question
How can an operation that is naturally defined for a whole sequence be implemented efficiently on an endless stream?

## Slide 4
DFT review: a finite set of frequency samples
DFT
0:03–0:09
WEEK 10 • TIME-FREQUENCY ANALYSIS
X[k] = Σₙ₌₀ᴺ⁻¹ x[n] e^(−j2πkn/N), k = 0,…,N−1
• The DFT is exactly the DTFT of the N-sample finite record evaluated at ωₖ = 2πk/N.
• The inverse DFT reconstructs those N time samples exactly.
• The DFT assumes an N-periodic extension when we interpret algebra such as convolution.
Do not confuse
A larger FFT can sample the same finite-record DTFT more densely, but zero-padding does not create new time-domain information.

## Slide 6
The DFT samples the DTFT
DFT
0:09–0:14
WEEK 10 • TIME-FREQUENCY ANALYSIS
Reading the figure
The smooth curve is the finite record’s DTFT. The dots are the 32 DFT samples. An FFT is an algorithm for computing these samples efficiently.
Frequency grid: ωₖ = 2πk/N

## Slide 7
Why the FFT matters computationally
DFT
0:14–0:20
WEEK 10 • TIME-FREQUENCY ANALYSIS
Direct DFT: approximately O(N²) operations
FFT: approximately O(N log₂N) operations
• This difference becomes decisive for long FIR filters and repeated streaming blocks.
• The FFT does not change the transform—it changes the computational algorithm.
• Fast convolution exploits the convolution theorem plus the FFT.
Example
For N = 4096, N² ≈ 16.8 million while N log₂N ≈ 49 thousand scale operations (constant factors omitted).

## Slide 9: DFT Computation

## Slide 10: DFT Computation

## Slide 11
Linear convolution versus circular convolution
CONVOLUTION
0:20–0:27
WEEK 10 • TIME-FREQUENCY ANALYSIS
Linear: y[n] = Σₘ x[m] h[n−m]
N-point circular: y_N[n] = Σₘ₌₀ᴺ⁻¹ x[m] h[(n−m) mod N]
• Linear convolution has length Lx + Lh − 1 for finite sequences.
• Circular convolution wraps samples modulo N.
• DFT multiplication corresponds to circular convolution of the N-point sequences.
Key issue
If N is too small, the tail of the linear convolution wraps onto the beginning.

## Slide 12
Wrap-around is the error
CONVOLUTION
0:27–0:32
WEEK 10 • TIME-FREQUENCY ANALYSIS
What happened?
The N=4 circular result folds the samples that belong at n ≥ 4 back into n = 0,1,… .
Circular is not “wrong”—it is a different operation.

## Slide 13
Zero-padding makes DFT convolution linear
CONVOLUTION
0:32–0:38
WEEK 10 • TIME-FREQUENCY ANALYSIS
Choose an FFT length satisfying
NFFT ≥ Lx + Lh − 1
• Pad both x[n] and h[n] to NFFT.
• Multiply their NFFT-point DFTs.
• Take the inverse DFT.
• The first Lx + Lh − 1 samples equal the linear convolution.
Example
Lx = 1000 and Lh = 129 require at least 1128 points. In practice, 2048 may be chosen for FFT efficiency.

## Slide 14
Concept check: padding requirement
CONCEPT CHECK
0:38–0:40
WEEK 10 • TIME-FREQUENCY ANALYSIS
x[n] has length 80 and h[n] has length 33. What is the minimum FFT size for one-shot FFT-based linear convolution?

## Slide 15
Concept check: padding requirement
CONCEPT CHECK
0:38–0:40
WEEK 10 • TIME-FREQUENCY ANALYSIS
x[n] has length 80 and h[n] has length 33. What is the minimum FFT size for one-shot FFT-based linear convolution?
Good answer
NFFT ≥ 80 + 33 − 1 = 112. Any NFFT of at least 112 works mathematically; an implementation may choose 128.

## Slide 16
Why block processing is needed
STREAMING
0:40–0:46
WEEK 10 • TIME-FREQUENCY ANALYSIS
• A microphone, sensor, or radio stream does not end so that we can take one giant FFT.
• We process finite blocks as they arrive.
• Each block must still reproduce the same linear FIR filtering result.
• Block length affects throughput, latency, memory, and FFT efficiency.
ML connection
Real-time inference often begins with streaming DSP: filtering, resampling, denoising, framing, and feature extraction.

## Slide 17
Overlap-Add: filter independent input blocks
OVERLAP-ADD
0:46–0:54
WEEK 10 • TIME-FREQUENCY ANALYSIS
1. Split x[n] into non-overlapping blocks of B samples.
2. Zero-pad each block and h[n] so NFFT ≥ B + Lh − 1.
3. FFT → multiply by H[k] → IFFT.
4. Add the overlapping output tails.
Each block produces B + Lh − 1 valid linear-convolution samples.
Why “add”?
Adjacent block convolutions overlap in time because the FIR has memory. Those overlapping contributions must be summed.

## Slide 19
Overlap-Add Example B=3, Lh=2, NFFT=B+Lh-1=4, h[n]=[h0, h1]
x[n]-> x0 x1 x2 x3 x4 x5 x6 x7 x8 x9 ……
*h[n] *h[n] *h[n] *h[n]
x0h0 x0h1 x3h0 x3h1 x6h0 x6h1 x9h0 ……
x1h0 x1h1 x4h0 x4h1 x7h0 x7h1
x2h0 x2h1 x5h0 x5h1 x8h0 x8h1
----------------------------- ----------------------------- ----------------------------- -------
x0h0 x0h1+x1h0 x1h1+x2h0 x2h1 x3h0 x3h1+x4h0 x4h1+x5h0 x5h1 x6h0 x6h1+x7h0 x7h1+x8h0 x8h1 x9h0 ……
overlap x0h0 x0h1+x1h0 x1h1+x2h0 x2h1
and add x3h0 x3h1+x4h0 x4h1+x5h0 x5h1
x6h0 x6h1+x7h0 x7h1+x8h0 x8h1
x9h0 ……
y[n]-> x0h0 x0h1+x1h0 x1h1+x2h0 x2h1+x3h0 x3h1+x4h0 x4h1+x5h0 x5h1+x6h0 x6h1+x7h0 x7h1+x8h0 x8h1+x9h0 ……

## Slide 20
Overlap-Add gives the same FIR output
OVERLAP-ADD
0:54–0:58
WEEK 10 • TIME-FREQUENCY ANALYSIS
Verification
The direct time-domain FIR and FFT overlap-add traces lie on top of one another to numerical precision.
This equivalence should be a coding unit test.

## Slide 21
Overlap-Save: overlap the input, discard invalid outputs
OVERLAP-SAVE
0:58–1:06
WEEK 10 • TIME-FREQUENCY ANALYSIS
• Choose an FFT size NFFT and FIR length Lh.
• Each input block contains Lh − 1 old samples plus new samples.
• Perform NFFT-point circular convolution.
• Discard the first Lh − 1 output samples, which contain time-aliasing contamination.
• Keep the remaining NFFT − Lh + 1 valid samples.
Why “save”?
We save only the uncontaminated portion of each circular-convolution block and concatenate those portions.
Contrast
OLA overlaps and adds outputs. OLS overlaps inputs and discards corrupted outputs.

## Slide 23
Overlap-Save Example B=3, Lh=2, NFFT=B+Lh-1=4, h[n]=[h0, h1]
x2 overlap x5 overlap
x[n]-> 0 x0 x1 x2 x2 x3 x4 x5 x5 x6 x7 x8
*h[n] *h[n] *h[n]
0h0 0h1 x2h0 x2h1 x5h0 x5h1
x0h0 x0h1 x3h0 x3h1 x6h0 x6h1
x1h0 x1h1 x4h0 x4h1 x7h0 x7h1
x2h0 x2h1 x5h0 x5h1 x8h0 x8h1
------------------------------- --------------------------------------- ---------------------------------------
0 x0h0 x0h1+x1h0 x1h1+x2h0 x2h1 x2h0 x2h1+x3h0 x3h1+x4h0 x4h1+x5h0 x5h1 x5h0 x5h1+x6h0 x6h1+x7h0 x7h1+x8h0 x8h1
wrap 0+x2h1 x0h0 x0h1+x1h0 x1h1+x2h0 x2h0+x5h1 x2h1+x3h0 x3h1+x4h0 x4h1+x5h0 x5h0+x8h1 x5h1+x6h0 x6h1+x7h0 x7h1+x8h0
mod NFFT
Discard and concatenate
y[n]-> x0h0 x0h1+x1h0 x1h1+x2h0 x2h1+x3h0 x3h1+x4h0 x4h1+x5h0 x5h1+x6h0 x6h1+x7h0 x7h1+x8h0 ……

## Slide 24
OLA versus OLS: engineering trade-offs
STREAMING
1:06–1:10
WEEK 10 • TIME-FREQUENCY ANALYSIS
Overlap-Add
• Simple conceptual decomposition.
• Needs an output accumulation buffer.
• Input blocks are non-overlapping.
Overlap-Save
• Input blocks overlap by Lh − 1.
• No output addition step.
• Discard first Lh − 1 samples per block.
Both
Reuse H[k] for every block and can be much faster than direct convolution for long FIR filters.

## Slide 25
Choosing FFT and block sizes
STREAMING
1:10–1:13
WEEK 10 • TIME-FREQUENCY ANALYSIS
• Larger FFTs often improve arithmetic efficiency per sample but increase buffering latency.
• Short blocks reduce latency but increase FFT overhead.
• Choose NFFT using measured platform performance, not only asymptotic complexity.
• On an edge device, memory movement and cache behavior can matter as much as multiply counts.
Design question
A classifier needs 10-ms latency. Would a huge “efficient” FFT block still be acceptable? No—the end-to-end latency constraint dominates.

## Slide 26
ML pipeline connection
ML BRIDGE
1:13–1:14
WEEK 10 • TIME-FREQUENCY ANALYSIS
stream → fast FIR / resampling → framing → features → model
• Fast convolution lets expensive preprocessing run continuously without changing the filter response.
• The same block boundaries should not create artifacts that leak into ML features.
• Streaming DSP and streaming inference must share latency and buffer budgets.
Think like a system designer
Accuracy, throughput, latency, and numerical equivalence all matter.

## Slide 27
Lecture 11 wrap-up
WRAP-UP
1:14–1:15
WEEK 10 • TIME-FREQUENCY ANALYSIS
• The DFT samples the finite-record DTFT.
• DFT multiplication gives circular convolution.
• Zero-padding prevents wrap-around and recovers linear convolution.
• Overlap-add and overlap-save extend FFT convolution to endless streams.
• Block size is both a DSP and systems-design parameter.
Exit ticket
Why is NFFT ≥ B + Lh − 1 required in overlap-add, and what fails if NFFT is smaller?

## Slide 28
Two Reasons to Consider Zero Padding for DFT/FFTs

## Slide 29
Two Sinusoids Close in Frequency

## Slide 30
Two Sinusoids Close in Frequency
Blue to orange: Zero padding increases graph resolution but not frequency resolution.
Orange to green: More signal samples increases frequency resolution.