## Slide 1
DSP & MACHINE LEARNING
Audio Signal Analysis
Bridging the gap from the DTFT to practical STFTs and Power Spectra.

## Slide 2
The Ideal vs. The Practical
Discrete-Time Fourier Transform (DTFT)
X(ejω) = ∑ x[n] e-jωn
BEAUTIFUL MATH. UNCOMPUTABLE REALITY.
Infinite duration: Requires signal knowledge from beginning to end.
Continuous frequency: Results in an uncomputable continuous spectrum.
Hardware limitation: Computers have finite memory arrays.

## Slide 3
Bridging to the DFT
Sampling the Spectrum
We solve the continuous frequency problem by sampling the DTFT at N equally spaced points between 0 and 2π.
X[k] = ∑ x[n] e-j(2π/N)kn

## Slide 4
The Cost of Truncation
Spectral Leakage
Finite Observation Extracting N samples equals multiplying by a rectangular window.
Time-Frequency Duality Multiplication in time is convolution in frequency.
The Sinc Smear Energy bleeds into adjacent frequency bins.

## Slide 5
STOCHASTIC SIGNALS
Power Spectral Density (PSD)
Wiener-Khinchin Theorem: PSD is the Fourier transform of the autocorrelation sequence.
1
Audio signals have infinite energy over time.
2
We analyze finite power distribution across frequencies instead.
Sxx(ω) = ∑ rxx[m] e-jωm

## Slide 6
Estimating PSD: The Periodogram
DIRECT COMPUTATION
P[k] = (1/N) |X[k]|2
Efficient
Computed via Fast Fourier Transform.
High Variance
Noisy estimate without averaging (Welch's).

## Slide 7
THE REALITY OF AUDIO
Signals are Non-Stationary
A global DFT reveals exactly what frequencies exist, but completely destroys when they occurred.

## Slide 8
The Short-Time Fourier Transform
Mapping the time-frequency landscape.

## Slide 9
The STFT Pipeline
1. Frame
Extract localized segment.
2. Window
Taper edges to zero.
3. Transform
Compute local spectrum.

## Slide 10
Maintaining Continuity
The Issue
Windowing heavily suppresses data at frame edges. Contiguous frames drop energy.
The Solution
Overlap frames (typically 50-75%). A smaller Hop Size increases temporal density.

## Slide 11
THE UNCERTAINTY PRINCIPLE
Time vs. Frequency Resolution
Long Window (N ↑)
Short Window (N ↓)
Time Resolution: Poor localization.
Frequency Resolution: High precision.
Best for: Stable harmonic chords.
Time Resolution: Sharp localization.
Frequency Resolution: Smeared bands.
Best for: Percussion and transients.

## Slide 12
Visualizing the STFT: Spectrogram
STFT Matrix Magnitude: |X(t, f)|
Y: Frequency
X: Time
Color: Power

## Slide 13
Interactive Session
Open Jupyter Notebook:
audio_stft_demo.ipynb
Task 1
Vary window size.
Task 2
Observe hop size impact.
Task 3
Listen to synthesis.

## Slide 14
Questions?
Next Class: Overlap-Add Synthesis & Filterbanks

## Slide 15
Image Sources
https://www.electronics-lab.com/wp-content/uploads/2023/09/FIGURE-3_DFT.png
Source: www.electronics-lab.com
https://community.sw.siemens.com/servlet/rtaImage?eid=ka6KZ00000000iN&feoid=00N4O000006Yxpf&refid=0EM4O000001130x
Source: community.sw.siemens.com
https://www.masteringbox.com/wp-content/uploads/2025/03/Frequency-tab-2048x1016.png
Source: www.masteringbox.com
https://www.numerical-tours.com/matlab/audio_1_processing/index_06.png
Source: www.numerical-tours.com
https://media.geeksforgeeks.org/wp-content/uploads/20231011105320/ad3-(1).png
Source: www.geeksforgeeks.org