## Slide 1
The DTFT and the DFT
01
A finite spectrum for a finite record
Senior electrical engineering · Digital signal processing
30-minute introduction
Notes: TIME: 0:00–0:30 (0.5 minutes). Opening: Students already know the DTFT. Ask what a computer should return when given a block of samples. Establish that this lecture uses angular frequency in radians per sample and the usual unscaled forward DFT with 1/N in the inverse. The 14 core slides total 30 minutes. Slides 15–16 are optional.

## Slide 2
DTFT review
02
Notation: X(ω) denotes the DTFT, usually written X(exp(jω)).
X(ω) =
∑
∞
n = −∞
x[n] exp(−jωn)
Discrete time index n, continuous frequency ω
Periodicity: X(ω + 2π) = X(ω)
One period contains the full DTFT.
Notes: TIME: 0:30–2:30 (2 minutes). Use X(ω) as shorthand for the conventional X(e^{jω}). Both refer to the same function of angular frequency. The DTFT is continuous in its frequency argument even though time is discrete. The sequence may have finite or infinite support. Because exp(−j2πn)=1 for integer n, the DTFT repeats every 2π. Ask: does discrete time imply discrete frequency? Answer: no. Assume the DTFT exists in the appropriate sense.

## Slide 3
A finite observation changes the signal
03
Finite record: xᵣ[n] = x[n] for 0 ≤ n ≤ N − 1, and 0 otherwise
Xᵣ(ω) =
∑
N − 1
n = 0
xᵣ[n] exp(−jωn)
The sum is finite. Its frequency argument remains continuous.
Windowing determines which signal’s spectrum we compute.
Notes: TIME: 2:30–4:30 (2 minutes). Distinguish the original x[n] from the observed record xᵣ[n]. Assume a rectangular window starting at zero. The DTFT of this record is still continuous in frequency. Truncating a longer signal changes the spectrum: multiplication in time corresponds to periodic convolution in frequency. Do not derive the convolution here. If x already has support within the record, no truncation occurs. Later leakage plots illustrate the window effect.

## Slide 4
Equally spaced DTFT samples define the DFT
04
ωₖ = 2πk/N, k = 0, 1, …, N − 1
X[k] = Xᵣ(ωₖ)
X[k] =
∑
N − 1
n = 0
xᵣ[n] exp(−j2πkn/N)
The N-point DFT gives N exact samples of the record’s DTFT.
Notes: TIME: 4:30–7:30 (3 minutes). Derive the DFT by substituting ωₖ=2πk/N into the finite DTFT on slide 3. Stress that the equality is exact. It is the DTFT of the finite record, not generally the original infinite sequence. Explain that N complex frequency values can describe N complex time values. k=N would repeat k=0, so only k=0,...,N−1 are unique. N can exceed the nonzero record length if we append zeros.

## Slide 5
A DTFT curve and its DFT samples
05
xᵣ = [1, 1, 1, 1, 0, 0, 0, 0], N = 8
Chart: Magnitude
8-point DFT | 4 | 2.6131 | 0 | 1.0824 | 0 | 1.0824 | 0 | 2.6131
Frequency sampling keeps values at a selected grid.
Notes: TIME: 7:30–9:30 (2 minutes). Example: xᵣ=[1,1,1,1,0,0,0,0], N=8. The finite DTFT is 1+exp(−jω)+exp(−j2ω)+exp(−j3ω). Blue curve is the magnitude of this finite DTFT evaluated densely. Orange points are magnitudes at k/8. Values for k=0,...,7 are approximately [4,2.6131,0,1.0824,0,1.0824,0,2.6131]. Emphasize that the DFT points lie on the curve. The complex DFT samples also contain phase, which this magnitude plot omits. All plot values follow directly from the displayed finite record.

## Slide 6
Frequency bins and physical units
06
Δω = 2π/N Δf = fₛ/N
fₖ = k fₛ/N (before wrapping)
Example: N = 8, fₛ = 8 kHz gives Δf = 1 kHz
Bin k = 1: +1 kHz Bin k = 7: −1 kHz
For real records: X[N − k] = X[k]*, 1 ≤ k ≤ N − 1
Bins repeat modulo N, just as DTFT frequency repeats modulo 2π.
Notes: TIME: 9:30–11:30 (2 minutes). Each k is a frequency bin. For a sampled continuous-time signal at sampling frequency fₛ, fₖ=k fₛ/N before wrapping. Frequencies above fₛ/2 represent negative frequencies. Example N=8 and fₛ=8000 Hz: bin spacing 1000 Hz. k=0,1,2,3,4,5,6,7 correspond to signed [0,1000,2000,3000,−4000,−3000,−2000,−1000] Hz. The Nyquist bin at k=4 may equally be called +4000 Hz. For even N, k=N/2 is this special bin. For real x, X[N−k]=X[k]*; DC and Nyquist are real. fftshift reorders bins without changing values.

## Slide 7
A four-point DFT by hand
07
x = [1, 2, 0, 0], N = 4
X[k] = 1 + 2 exp(−jπk/2)
k | 0 | 1 | 2 | 3
X[k] | 3 | 1 − 2j | −1 | 1 + 2j
X[0] is the sample sum. Real input gives conjugate symmetry.
Notes: TIME: 11:30–13:30 (2 minutes). Give students 15 seconds to compute X[0] as the sum of samples. Here x=[1,2,0,0]. The transform is X[k]=1+2 exp(−jπk/2). Substitute k=0,1,2,3. Values are [3,1−2j,−1,1+2j]. The conjugate pair is consistent with real input. Frequency-bin values are generally complex even for real input. This uses the unscaled forward transform convention. If time allows, X[2]=1−2=−1 is a quick second check.

## Slide 8
The inverse DFT recovers the record
08
xᵣ[n] = (1/N)
∑
N − 1
k = 0
X[k] exp(+j2πkn/N)
For 0 ≤ n ≤ N − 1, the IDFT returns the original N samples.
Orthogonality over one period
∑
N − 1
k = 0
exp(j2πk(n − m)/N)
= N if n ≡ m (mod N), otherwise 0
Notes: TIME: 13:30–16:30 (3 minutes). Present the inverse formula with a 1/N factor and the opposite sign. Sketch why it works: substituting the forward DFT into the inverse creates a sum over k of exp(j2πk(n−m)/N). That sum equals N when n−m is a multiple of N and zero otherwise. For n,m in 0,...,N−1, only n=m survives. Thus xᵣ[n] is recovered exactly apart from numerical rounding. Orthogonality is the reason the N frequency samples suffice for an N-sample block. Ask students what happens at n=N. The expression repeats xᵣ[0], which motivates the next slide.

## Slide 9
The periodic interpretation
09
x̃[n] = xᵣ[n mod N]
One record: [1, 2, 0, 0]
Periodic extension:
… 1, 2, 0, 0 1, 2, 0, 0 1, 2, 0, 0 …
The DFT describes one period of this extension.
Notes: TIME: 16:30–18:30 (2 minutes). Clarify that the recorded sequence may be zero outside its block. Extending the IDFT synthesis formula to every integer n instead defines its N-periodic extension. This distinction avoids saying that the original physical signal is periodic. The displayed repeating block is x=[1,2,0,0] for N=4. The synthesis frequencies complete integer numbers of cycles per block. DFT values divided by N are the discrete Fourier-series coefficients of the periodic extension under the usual Fourier-series convention.

## Slide 10
Concept check: what does the DFT sample?
10
We keep N samples of a longer sequence and compute its DFT.
A It exactly samples the original sequence’s DTFT.
B A finite record has a discrete-frequency DTFT.
C It exactly samples the finite record’s DTFT.
D A larger DFT recovers the discarded time samples.
Notes: TIME: 18:30–20:00 (1.5 minutes). Give 20 seconds to vote and 30 seconds for students to explain to a neighbor. Correct answer C. Truncation creates a new finite record. Its N-point DFT exactly samples its DTFT at 2πk/N. A is generally false because samples outside the record contribute to the original DTFT. B is false because ω remains continuous in the finite DTFT. D confuses dense frequency sampling with recovering missing time data. Use the remaining time to ask which step changed the signal. Answer: truncation/windowing. Do not advance to the backup answer slide during the core sequence.

## Slide 11
DFT multiplication gives circular convolution
11
IDFT{X[k]H[k]} = N-point circular convolution
y[n] =
∑
N − 1
m = 0
x[m] h[(n − m) mod N]
Example: [1, 1] * [1, 1] = [1, 2, 1] (linear)
A 2-point DFT product gives [2, 2] (circular)
For linear convolution: choose N ≥ Lₓ + Lₕ − 1.
Notes: TIME: 20:00–22:00 (2 minutes). This slide previews a consequence of periodicity rather than developing the full convolution theorem. The inverse DFT of the product X[k]H[k] gives N-point circular convolution. Indices wrap modulo N. Example x=[1,1], h=[1,1] have linear convolution [1,2,1]. With a 2-point DFT the tail wraps into the first sample, giving [2,2]. Padding both sequences to at least Lₓ+Lₕ−1=3 makes the corresponding circular convolution equal the linear result in the output block. This prevents time wraparound; it differs from increasing spectral resolving power.

## Slide 12
An off-grid tone spreads across bins
12
32-sample complex tone: exp(j2πan/32)
a = 5: exactly on a bin
a = 5.5: between bins
Chart: Magnitude / 32
DFT bins | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Magnitude / 32
DFT bins | 0.060786 | 0.07309 | 0.09276 | 0.12861 | 0.21298 | 0.63688 | 0.63688 | 0.21298 | 0.12861 | 0.09276 | 0.07309 | 0.060786 | 0.052459
The window’s spectrum explains leakage and bin alignment.
Notes: TIME: 22:00–24:30 (2.5 minutes). Use complex exponentials to isolate one spectral component. In both plots take 32 samples, n=0,...,31. Left tone exp(j2π·5n/32) gives a DFT with one nonzero bin at k=5, magnitude 32. Right tone exp(j2π·5.5n/32) gives multiple nonzero bins. Magnitudes are normalized by 32. The continuous blue curve in both cases is the finite record DTFT magnitude. Orange points sample it at k/32. Windowing an infinite tone gives a shifted rectangular-window spectrum. On-grid placement aligns other bins with its zeros. Leakage reflects finite observation and bin alignment. Emphasize that the underlying DTFT has a main lobe and sidelobes in both cases, even when the on-grid DFT samples only one peak.

## Slide 13
Zero padding samples the same DTFT more densely
13
Record length L = 16. DFT length M = 16 or 64.
Chart: Magnitude / 16
M = 16 (large) | 0.096013 | 0.13093 | 0.21898 | 0.75761 | 0.50572 | 0.19236 | 0.12165 | 0.091525 | 0.075691
M = 64 (small) | 0.096013 | 0.048937 | 0.035823 | 0.11201 | 0.13093 | 0.069252 | 0.052991 | 0.17493 | 0.21898 | 0.12673 | 0.10986 | 0.43752 | 0.75761 | 0.96354 | 0.98369 | 0.81097 | 0.50572 | 0.1708 | 0.09012 | 0.21257 | 0.19236 | 0.079858 | 0.048194 | 0.12508 | 0.12165 | 0.053451 | 0.033777 | 0.091089 | 0.091525 | 0.041363 | 0.026793 | 0.073857 | 0.075691
Finer bin spacing
Δω = 2π/M
The main-lobe
width stays fixed.
A longer measured record can separate closer frequencies.
Notes: TIME: 24:30–26:30 (2 minutes). Keep the same 16 nonzero samples x[n]=exp(j2π·3.4n/16), n=0,...,15. Compare M=16 versus M=64 by appending 48 zeros. Chart magnitudes are divided by 16 in both cases. The DTFT does not change because added zeros contribute nothing. The bin grid becomes finer, Δω=2π/M. A finer plot supports peak interpolation but does not narrow the window main lobe or improve the ability to separate nearby tones for this unchanged observation. More measured samples extend the observation and can improve resolving power. Keep record length L and DFT length M distinct.

## Slide 14
The transition in one equation
14
X[k] = Xᵣ(2πk/N)
Windowing selects the record. Frequency sampling defines the DFT.
The IDFT recovers the block and extends it periodically.
An FFT computes the DFT efficiently.
Exit ticket
16 samples at 8 kHz, padded to 64: what is the new bin spacing?
Does padding improve the ability to separate nearby tones? Why?
Notes: TIME: 26:30–30:00 (3.5 minutes). Recap for 60 seconds, exit ticket for 90 seconds, then discuss the answers for 60 seconds. Ask both prompts. Expected answers: (1) Δf=8000/64=125 Hz, compared with 500 Hz before padding. (2) The observation duration and window main-lobe width do not change, so denser bins alone do not improve the ability to separate nearby tones. FFT is an algorithm for computing the same DFT efficiently. Answer reference is slide 15

## Slide 15
Answers to the concept checks
15
Concept check (slide 10)
C: The DFT samples the finite record’s DTFT.
Truncation determines which spectrum the DFT samples.
Exit ticket (slide 14)
Δf = 8000/64 = 125 Hz
The same observation gives the same DTFT main-lobe width.
Notes: OPTIONAL BACKUP. Outside the 30-minute sequence. Optional answer reference. Concept check on slide 10: C. Windowing changes the signal. Frequency sampling then gives exact values of that finite record’s DTFT. Exit ticket on slide 14: 125 Hz. Before padding the 16-point bin spacing is 500 Hz. Zero padding adds no measured samples and leaves the DTFT main-lobe width unchanged. It can provide a finer display and help estimate the peak location. DFT computation and FFT algorithm are different concepts.

## Slide 16
Frequency sampling and time aliasing
16
X[k] = X(2πk/N) for an infinite sequence x[n]
IDFT{X[k]} =
∑
∞
ℓ = −∞
x[n + ℓN]
Uniform frequency sampling creates periodic sums in time.
Overlapping copies produce time aliasing.
A record supported on 0, …, N − 1 has no overlap.
Notes: OPTIONAL BACKUP. Outside the 30-minute sequence. Optional derivation beyond the 30-minute introduction. Suppose X(ω) is the DTFT of an infinite absolutely summable sequence. Define X[k]=X(2πk/N). Insert the DTFT sum into the IDFT and interchange sums. Orthogonality leaves all time indices equal to n modulo N, giving the periodic sum shown. A finite record with support in 0,...,N−1 reduces this sum to its N-periodic extension. For an infinite sequence, the periodic copies can overlap, producing time aliasing. This is why sampling the original infinite sequence DTFT is different from taking a DFT after truncation. General theory follows the DTFT/DFT development in Oppenheim and Schafer, Discrete-Time Signal Processing, DFT chapter (number depends on edition). All charts in this deck are original numerical evaluations of the displayed finite sums.