## Slide 1
DSP & MACHINE LEARNING
Reconstruction & Filterbanks
From STFT back to the time domain.

## Slide 2
The Reconstruction Problem
We analyzed the signal. Now what?
The STFT maps a 1D time signal to a 2D time-frequency matrix.
If we modify the STFT (e.g., noise reduction, pitch shifting), how do we return to a continuous 1D audio signal?
x[n] ⇄ X(m, ω)
We cannot simply concatenate inverse DFTs.

## Slide 3
THE BOUNDARY PROBLEM
Windowing Destroys Edges
The Tapering Effect
Analysis windows (Hann, Hamming) force the signal edges to zero to prevent spectral leakage.
Amplitude Modulation
Simply placing inverse-transformed frames side-by-side results in severe pulsing (tremolo) at frame boundaries.

## Slide 4
The Constant Overlap-Add (COLA) Constraint
∑ = 1
The shifted windows must sum to exactly 1.0 everywhere to ensure perfect reconstruction without amplitude distortion.

## Slide 5
The Overlap-Add Process
1. Inverse DFT
Transform modified spectra back to time-domain frames.
2. Shift
Align frames using original hop size.
3. Add
Sum overlapping samples to reconstruct continuous signal.

## Slide 6
Perfect Reconstruction
Hann windows overlapping at 50% hop size sum to a constant DC value.
[Insert Overlap-Add Diagram Here]

## Slide 7
Filterbank Interpretation
An alternative view of the STFT.

## Slide 8
Two Views of the STFT
Transform View
Filterbank View
Operation: Block-by-block FFT.
Focus: Frequency spectrum at a specific time index.
Implementation: Highly efficient (FFT).
Operation: Parallel bandpass filtering.
Focus: Time evolution of a specific frequency bin.
Implementation: Conceptual framework for audio effects.

## Slide 9
The STFT is a Filterbank
Each frequency bin k in the STFT can be viewed as the output of a discrete filter.
The Base Filter:
The chosen window function acts as a lowpass filter prototype.
The Modulation:
Multiplying by complex exponentials shifts this lowpass filter to create N parallel bandpass filters.
Filter 0 (Lowpass)
Filter 1 (Bandpass)
...
Filter N/2 (Nyquist)

## Slide 10
APPLICATIONS
Spectral Processing
Noise Reduction
Zero out STFT bins containing stationary background noise before OLA reconstruction.
Compression
Discard low-energy bins (lossy compression like MP3 relies on psychoacoustic masking models applied to the STFT).
Pitch Shifting
Shift frequency bins up or down while maintaining the time envelope (Phase Vocoder).

## Slide 11
The Phase Problem
Modifying STFT magnitudes is easy. Modifying phases without causing destructive interference during OLA reconstruction is hard.
*Advanced topic: Phase unwrapping and the Phase Vocoder algorithm.*

## Slide 12
Questions?
Next Assignment: Implement a spectral noise gate.