## Slide 1
ECEN 4/5632 Theory and Application of Digital Filters
Lecture 7, 9-15-26
Peter Mathys*
* With generous help from Gemini Pro and ChatGPT

## Slide 2
WEEK 4 ● LECTURE 7
FIR Filter Design, Windowing, & 1D Convolutions
From ideal frequency responses to fixed or learnable convolution kernels
FIR / phase
→
ideal LPF
→
window method
→
Conv1d
75 minutes • senior + first-year graduate ECE
Oppenheim & Schafer + Raschka

## Slide 3
ROADMAP
Where this 75-minute lecture is going
2
0–10 min • FIR vs. IIR
Linear phase, group delay, and why waveform alignment can matter.
10–30 min • Ideal filter + Gibbs
Derive the sinc impulse response and see what truncation does.
30–55 min • Window method
Main-lobe width versus sidelobe attenuation.
55–75 min • DSP ↔ PyTorch
Implement fixed FIR taps with Conv1d; then ask what changes when weights are learned.
DSP bridge: a mathematically designed FIR and a neural 1-D convolution use the same sliding weighted sum.
Classical DSP supplies structure and constraints; machine learning either reuses that structure or learns parameters inside it.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 4
FIR VS. IIR
Same frequency-selective goal, different structures
3
FIR: feedforward
Finite impulse response. No feedback. Exact linear phase is available when the taps have the required symmetry.
IIR: recursive
Feedback permits sharp magnitude responses with fewer coefficients, but phase is generally nonlinear.
ML perspective
A fixed FIR can be the front end of an ML pipeline; a Conv1d layer uses the same local weighted sum but can make the coefficients trainable.
Do not oversell linear phase: it is valuable when temporal alignment and waveform shape should be preserved, but not every ML task requires it.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 6
LINEAR PHASE
Symmetric FIR taps give a constant delay
4
Physical interpretation
Every passband frequency component is delayed by the same number of samples, apart from sign-related phase jumps where the real amplitude term changes sign.
ML connection
If a transient shape is a feature, constant delay avoids frequency-dependent smearing before MFCCs, peaks, onsets, or time-localized descriptors are computed.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 8
LINEAR PHASE
Group delay is the more intuitive diagnostic
5
Read the plot
For a 41-tap symmetric FIR, the expected delay is
Good answer
“Linear phase does not mean zero delay. It means a delay that is approximately constant with frequency.”
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 9
CONCEPT CHECK
What would nonlinear phase do to a transient?
6
Question
Two filters have nearly identical magnitude responses. One has constant group delay; the other has strongly frequency-dependent group delay. What can differ at the output?
Good answer
The spectra can have almost the same magnitudes while the waveform shapes differ because frequency components arrive with different delays.
Strong answer
That distortion can alter time-localized features such as onset shape or peak timing. Whether it harms an ML model depends on what features and invariances the model uses.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 10
IDEAL LOWPASS
Start in the frequency domain
7
−ωc
ωc
1
Engineering dream
Perfectly flat passband, zero stopband, and an infinitely sharp transition.
Reality
The price is an infinite-duration, noncausal impulse response.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 11
IDEAL LOWPASS
Inverse DTFT produces the sinc impulse response
8
Interpretation
A brick-wall frequency response requires a sinc extending forever in both time directions.
Senior/grad expectation
Students should be able to derive the sinc from the inverse DTFT, not only quote the result.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 12
IDEAL LOWPASS
The ideal impulse response is infinite and two-sided
9
Problem 1: infinite length
A finite processor cannot store or multiply by infinitely many taps.
Problem 2: noncausal
Samples for negative time imply dependence on future inputs unless we delay/shift the finite approximation.
What we will do
Truncate the sinc, shift it to be causal, and shape the truncation with a window.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 13
FINITE FIR
Center first, then shift to a causal tap sequence
10
For an FIR of order M with M+1 taps, centering the ideal response at M/2 gives the symmetry needed for linear phase.
Example
For N = 51 taps, M = 50 and the delay is 25 samples.
Important
The shift changes phase, not magnitude. We are making the finite approximation causal by accepting a fixed delay.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 14
GIBBS PHENOMENON
Rectangular truncation is simple—but its sidelobes are not
11
Time-domain action
The rectangular window keeps a finite block of sinc samples and sets everything else to zero.
Frequency-domain consequence
Abrupt truncation has strong sidelobes. Convolution with the rectangular-window spectrum creates oscillatory passband/stopband ripple.
A common misconception: “make the filter longer and the Gibbs ripple disappears.”
A longer rectangular window makes the ripple region narrower, but the limiting peak overshoot near the discontinuity does not go to zero.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 15
GIBBS PHENOMENON
Increasing length narrows the transition but does not eliminate overshoot
12
Read the plot
As N increases, the oscillation is compressed toward the cutoff.
But notice
The peak overshoot remains visible. Length and sidelobe level are different design knobs.
Next step
Use a smoother window to reduce sidelobes—accepting a wider transition.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 16
Gibbs’ Phenomenon

## Slide 17
WINDOW METHOD
Shape the truncation instead of switching it off abruptly
13
Key duality
Multiplication in time corresponds to periodic convolution in frequency.
Design intuition
A smoother time-domain taper lowers spectral sidelobes but broadens the window main lobe, which broadens the filter transition band.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 18
WINDOWS
Rectangular → Bartlett → Hann/Hamming → Blackman
14
Rectangular
Hardest edges; narrowest main lobe; high sidelobes.
Hann / Hamming
Smooth taper. Hamming is designed for a particularly low first sidelobe.
Blackman
Stronger taper and lower sidelobes, but a wider main lobe / transition.
“Hann” is the standard name; “Hanning” is common informal usage.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 19
Window Functions in Time and Frequency, N=51

## Slide 20
Window Functions in Time and Frequency, N=51

## Slide 21
WINDOW TRADEOFF
Main-lobe width versus sidelobe attenuation
15
Window
Approx. first sidelobe
Approx. main-lobe width*
Use when...
Rectangular
≈ −13 dB
≈ 4π/N
Narrow transition dominates
Bartlett
≈ −26 dB
≈ 8π/N
Simple triangular taper
Hann
≈ −31 dB
≈ 8π/N
Balanced spectral leakage
Hamming
≈ −43 dB
≈ 8π/N
Better first sidelobe suppression
Blackman
≈ −58 dB
≈ 12π/N
Strong stopband suppression
*Width between the first nulls; approximate asymptotic rules for equal window length.
Good answer
There is no universally “best” window. The specification decides how much transition width can be traded for stopband suppression.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 22
WINDOW TRADEOFF
Same length and cutoff; different transition/ripple behavior
16
Rectangular
Sharpest transition, worst sidelobes.
Hamming
A common compromise: wider transition, much lower first sidelobe.
Blackman
Strongest attenuation here, but broadest transition.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 23
Truncated and Windowed Ideal LPF, N=51,

## Slide 24
DESIGN EXAMPLE
A practical 51-tap Hamming lowpass
17
Specification sketch
Why Hamming?
We accept a somewhat wider transition in exchange for much better sidelobe rejection than rectangular truncation.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 25
FILTER LENGTH
Longer FIRs buy a narrower transition—at a cost
18
Increase N
More taps generally narrow the transition for the same window family.
But pay for it
More multiplies, more memory, and larger linear-phase delay
ML viewpoint
A longer convolution kernel also means a larger temporal receptive field and more learned parameters if the kernel is trainable.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 26
CONCEPT CHECK
Choose the design knob that matches the problem
19
A • Prompt
Stopband leakage is unacceptable, but transition width may be wider.
B • Prompt
Transition must be very narrow, but moderate ripple is acceptable.
C • Prompt
The filtered waveform must maintain relative timing across the passband.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 27
CONCEPT CHECK
Choose the design knob that matches the problem
19
A • Prompt
Stopband leakage is unacceptable, but transition width may be wider.
Good answer
Choose a stronger taper such as Blackman or increase length.
B • Prompt
Transition must be very narrow, but moderate ripple is acceptable.
Good answer
Rectangular can give a narrower main lobe for the same N; increasing N is another option.
C • Prompt
The filtered waveform must maintain relative timing across the passband.
Good answer
Use a linear-phase FIR or another phase-preserving strategy.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 28
DSP ↔ PYTORCH
A 1-D convolution is a sliding dot product
20
DSP view
The impulse response h[k] is designed to satisfy magnitude/phase specifications.
ML view
The same local dot product becomes a layer. The kernel may be initialized from DSP knowledge or learned from data.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 30
PYTORCH DETAIL
Conv1d uses cross-correlation ordering
21
To reproduce textbook causal FIR
Left-pad by M samples and reverse the coefficient order before calling Conv1d.
Good answer
The operation is not “wrong convolution”; deep-learning libraries use a correlation convention because the kernel is usually learned anyway.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka
(Local-window correlation)

## Slide 31
IMPLEMENTATION
Fixed FIR taps inside PyTorch
22
h = torch.tensor(h_np, dtype=torch.float32) x = torch.tensor(x_np).view(1, 1, -1) # causal textbook convolution kernel = h.flip(0).view(1, 1, -1) x_pad = F.pad(x, (len(h)-1, 0)) y = F.conv1d(x_pad, kernel)
Shape
Input is (N,C,L). A single mono signal is (1,1,L).
Fixed weights
Use a tensor or freeze a Conv1d layer so the taps do not receive gradient updates.
Learnable weights
Leave requires_grad=True and the same coefficients become trainable model parameters.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 32
TENSOR SHAPES
Batch, channel, and length carry physical meaning
23
N • Batch
Independent clips/examples processed together.
C • Channel
Mono, stereo, microphones, sensors, or learned feature maps.
L • Length
Discrete-time sample index / temporal extent.
Example: 32 stereo one-second clips at 16 kHz → (32, 2, 16000)
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 33
DEMONSTRATION
NumPy convolution and PyTorch Conv1d agree
24
Numerical check
The supplied script reports a maximum mismatch on the order of 10⁻⁷ in float32.
Teaching point
Same filter, same signal-processing operation. The distinction is whether the coefficients are fixed by design or optimized from data.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 34
DSP ↔ ML
Designed taps versus learned taps
25
Classical FIR design
Choose desired H(e^{jω}) → derive ideal h[n] → truncate/window → verify specifications.
Hybrid approach
Initialize Conv1d with a known bandpass/lowpass/filterbank and optionally fine-tune it.
Fully learned convolution
Choose kernel size and channels; backpropagation learns coefficients that reduce task loss.
The arithmetic is the same local weighted sum; the source of the weights is what changes.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 35
CONTEXT
Translate the classical vocabulary into ML vocabulary
26
DSP concept
Mathematical role
ML connection
FIR filter
feedforward delay line
Conv1d with fixed or learnable kernel
Tap h[k]
impulse-response coefficient
kernel / weight
Window
controls truncation spectrum
inductive constraint on kernel support; not the same as ML regularization
Linear phase
constant group delay
preserves relative temporal alignment
Filter length
transition width + delay
receptive field + parameter count
Nuance: a classical window is a deterministic spectral-design device; calling it “kernel regularization” is only an analogy.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 36
WRAP-UP
Lecture 7 synthesis
27
Linear phase
Symmetric FIR taps can provide constant group delay.
Ideal → practical
The brick-wall LPF becomes a sinc; finite implementation requires truncation and delay.
Window tradeoff
Lower sidelobes cost transition width.
PyTorch bridge
Conv1d performs the same local weighted sum; its weights may be fixed or learned.
Minute paper: What does a neural 1-D convolution add to the FIR operation itself?
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 37
WRAP-UP
Lecture 7 synthesis
27
Linear phase
Symmetric FIR taps can provide constant group delay.
Ideal → practical
The brick-wall LPF becomes a sinc; finite implementation requires truncation and delay.
Window tradeoff
Lower sidelobes cost transition width.
PyTorch bridge
Conv1d performs the same local weighted sum; its weights may be fixed or learned.
Minute paper: What does a neural 1-D convolution add to the FIR operation itself?
Strong answer
It does not change the local multiply-and-sum operation. It places that operation inside a trainable model so the kernel coefficients can be learned from a loss.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 38
HOMEWORK
Problems 1–4 • FIR and Conv1d
28
1 • Ideal LPF
Derive the sinc from the inverse DTFT; explain noncausality; find delay for N=41.
2 • Window tradeoff
Rectangular vs Hamming: transition, sidelobes, and Gibbs behavior.
3 • Linear phase
Show symmetric FIR form and derive constant group delay.
4 • Conv1d
Compute a 3-tap convolution and explain the PyTorch kernel flip.
Full worked solutions are included in Lectures7_8_Homework_Quiz_Solutions.md and the instructor package.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 39
INSTRUCTOR APPENDIX
Homework solutions • Problems 1–2
29
1 • Ideal LPF
Inverse DTFT gives the sinc; h_d[0]=ω_c/π. The ideal response is infinite and two-sided. For N=41, shift by 20 samples and τ_g=20.
2 • Windows
Rectangular: narrower transition but ≈−13 dB first sidelobe. Hamming: wider transition but ≈−43 dB first sidelobe. Increasing rectangular-window length narrows the Gibbs region; it does not eliminate peak overshoot.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka

## Slide 40
INSTRUCTOR APPENDIX
Homework solutions • Problems 3–4
30
3 • Symmetry
Pairing symmetric taps gives a real amplitude term times a pure delay. Therefore group delay is constant.
4 • Convolution
For h=[0.2,0.5,0.3] and x=[1,2,0,−1], the first four causal outputs are [0.2,0.9,1.3,0.4]. Conv1d uses correlation ordering, so flip the taps for textbook convolution.
DSP + Machine Learning • Lectures 7–8
Oppenheim & Schafer + Raschka